TECHNICAL BID OF :                                           (Firm Name)________________________________

PROJECT 52 : - PROVISION OF INTERNET LEASED LINE AT ARMY INSTITUTE OF MANAGEMENT NEW CAMPUS AT RAJARHAT,  KOLKATA

COMPLIANCE REPORT

| S. N | Technical Specification for Internet Leased Line Connection | Compiled (Yes/No) | Deviation if any |
| --- | --- | --- | --- |
| 1 | The bidder should be the Tier 1 national ISP and should have Category A ISP license from Govt. of India (Attach a copy of license) |  |  |
| 2 | The Internet Connectivity leased line should have fully dedicated (1:1), unshared & High Quality 50 Mbps symmetric bandwidth without any compression factor through Optical Fiber cable. |  |  |
| 3 | The ISP/bidder should have Nework Operation Centre (NOC) for trouble shooting around the clock |  |  |
| 4 | Internet Router Port at ISP Gateway for required Bandwidth and minimum 8 Public IP addresses of ipv4 pool and 8 Public IP addresses of ipv6 pool including Reverse Lookups configured at these IP's. |  |  |
| 5 | All the equipment’s supplied by the bidder should be capable of handing higher band width in case up gradation in required in the later stage. |  |  |
| 6 | Any Software and Hardware required establishing the purchased bandwidth will be provided by bidder to make leased line fully functional |  |  |
| 7 | The bidder should submit technical literature explaining the proposed implementation diagram with technical bid |  |  |
| 8 | The bidders should have Direct\toll free number to register complaints round the clock (24x7), Maintenance support service (24 hours and 7 days a week) |  |  |
| 9 | All the POPs from where the ILL bandwidth is provided to CWC should have redundancy of equipments, links, power, backhaul connectivity etc. Service provider needs to confirm it writing. |  |  |
| 10 | The ILL links should be available in full duplex mode. |  |  |
| 11 | IT Division of AIMK will consider the successful provision of the link subject to satisfactory Acceptance Test. The methodology for the test will be at the discretion of the Management. However, the same will be shared with the Bidder/SP. Average latency should not be more than 250 ms up to ISPs 1st Tier 1 peering point. Domestic Latency<80ms during peak traffic hours Internal Latency<250 ms during peak traffic hours Packet Loss<0.5% Facilities of testing above parameters will be provided by the Bidder/IPS |  |  |

Office Stamp

Signature

PROJECT : - PROVISION OF INTERNET LEASED LINE AT ARMY INSTITUTE OF MANAGEMENT NEW CAMPUS AT RAJARHAT,  KOLKATA

1.  The bid preferably be typed on letter head of the firm and authenticated by office stamp & signature on each page.

2. Rate quoted should be inclusive for providing Internet leased line connectivity on managed with router, uncompressed, unshared leased line (1:1), semantical bandwidth at AIMK New Campus, including installation, commissioning, testing etc.

| S No | Link Type | Service Type Managed/ Unmanaged | Bandwidth | Media | Standard Rate (Rs.) | One Time Charge (if any) (Rs) | Remarks(if any) |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | ILL | Managed | 50 MBPS | Fiber |  |  |  |
|  | Total |  |  |  |
|  | GST |  |  |  |
|  | Grand Total |  |  |  |

Office Stamp

Signature